## Slide 1: OUR TURTLEBOT
Jacob Steinthal and Sebastian Kittelmann

## Slide 2: Contents
Obstacle detection
Movement
Color detection
Collison detection

## Slide 3: Obstacle detection
Readings from LIDAR
Division into 20 cones
10 frontal cones are the only ones used
Smallest element in each cone is found
Invalid measurements are replaced with 3.5m

## Slide 4: Turning
Goes through cones in pairs
  Center cones are prioritized to optimize linear speed
  Pair corresponds to size of robot
Firstly looks for big opening – then smaller ones
  Then cones 2 and 3
If all else fails: turn right

## Slide 5: Linear and Angular Speed
Max linear speed: 0.21
Max angular speed: 1.28
Multiplied by factor dynamically set as linear functions of front distance

## Slide 6: Color Detection
Normalizing color readings
  Multiply with factor to make readings even
Thresholds for red and max values for green and blue
Must detect victim at least twice in the span of 8 readings
  Cannot detect new victim in same span
Robot slows down to detect colors better
Chart: Colour Distribution over Time

## Slide 7: Collison detection
Issues with just using LIDAR measurements
Used alternative methods
Method #1: Using the length of scan range as an indicator
Method #2: Using amount of NaN measurements as indicator
When colliding: Will start backing up
  Also happens when the robot is stuck
Chart: Edge NaN measurements
Chart: Length of scanning array